Interest Group Stream: Australian Optical Society

Development of a 100W, single frequency, CW Nd:YAG Laser

Damien MUDGE, Peter J. VEITCH, Jesper MUNCH, Murray W. HAMILTON, Martin OSTERMEYER, David HOSKEN, Aiden BROOKS

Department of Physics and Mathematical Physics, Adelaide University, Adelaide, SA 5005, Australia

Ph: +61-(08)-8303 5040

Fax: +61-(08)-8303 4380

Email: pveitch@physics.adelaide.edu.au

Oral presentation preferred.

High power, diode-laser-pumped, cw solid-state lasers with excellent beam quality, efficiency and reliability are required for demanding applications, including gravitational wave interferometry, where current additional requirements include single frequency, low noise and Nd:YAG.

Our approach is a chain of injection locked laser oscillators, theoretically capable of achieving the lowest noise possible. We use a single-frequency (100 mW) master laser to injection lock a medium-power (10 W) laser that in turn injection locks a 100 W laser. Injection locking requires an optimized, single mode, power slave laser at each stage. We shall describe the nearly completed 10 W brass-board laser, which will also be deployed at the ACIGA Test Facility at Gingin. We shall also describe our 100 W laser using a scalable diode pumping scheme, an active control of thermal lensing and a stable-unstable resonator. Initial tests showed mode control to be limited by thermal focusing and thermally induced birefringence in the Nd:YAG medium at 70 W output. Recent efforts have identified the source of the thermal lens and significantly reduced its magnitude, leading to a modified design. We shall present our latest results from the experiments to demonstrate single mode, single frequency laser at 100 W.